|  |  | EXCAVATION INSPECTION REPORT |
| --- | --- | --- |
| Date & Time: Location: Depth(1): List visual test(s) performed(2): List manual tests performed(2): SOIL(1) OR ROCK TYPE MAXIMUM ALLOWABLE SLOPE (H:V)(4) FOR EXCAVATION LESS THAN 20 FEET DEEP(3) Stable Rock – No visible fissures/cracks Vertical (90º ) Type A Soil - Cohesive soil with clay base ¾H:1V (53º )(2) (5) (No exposure to vibration) Type B Soil - Cohesive soil with a loam base (i.e., angular gravel, crushed rock, etc.) 1H:1V (45º ) (2) (5) Type C Soil - Granular soil including gravel and sand 1½H:1V (34º ) (2) (5) Other – Designed by a Registered Professional Engineer (RPE) (3) Note: The RPE’s written design criteria must be maintained locally and available for review Other Protection Systems(3) Acceptable Shoring: Timber Hydraulic Other From OSHA’s Charts Eng’d Data Acceptable Shielding: Single trench box Stacked trench boxes (Note: Top edge of shield must extend 18” above grade) Is the soil contaminated: Yes No If yes, with what? PPM Excavating in or near roads(6): Yes No If yes, has the Road Dept been notified: Yes No List all traffic control devices: Will water removal be needed: Yes No How will water be removed? Atmospheric check if over 4’ deep - Name of Equip? O2 % LFL / LEL % Spoil Pile - minimum 2 feet back: Yes No Comments: Competent person signature: Notes: Initiate inspections and take appropriate actions regardless of depth when soils indicate signs of stress or cave-in. Every inspection requires at least 1 visual test and 1 manual test. Sloping or benching excavations greater than 20 feet deep shall be designed & approved by a professional engineer registered within the same state as the excavation. Shoring & shield equipment used in excavations greater than 20 feet shall be designed & approved by a registered professional engineer. H denotes horizontal, V denotes vertical. All spoil piles, material or equipment must be a minimum of 2 feet from the edge of the excavation. A written Temporary Traffic Control Plan shall be developed and on site if any work is within 15 feet of a road. |