|  | EXCAVATION INSPECTION REPORT (Canada) |
| --- | --- |
| Date & Time: Location: Depth(1): List visual test(s) performed(2): List manual tests performed(2): SOIL(1) OR ROCK TYPE MAXIMUM ALLOWABLE SLOPE (H:V)(4) FOR EXCAVATION LESS THAN 6.10m DEEP(3) Type 1Soil – See Attachment A .305m H:.305mV(45º ) Type 2 Soil - See Attachment A .305m H:.305mV(45º )2) (5) Type 3 Soil - See Attachment A .305m H:.305mV(45º )2) (5) Type 4 Soil - See Attachment A 3mH:1mV (19º ) (2) (5) Other – Designed by a Registered Professional Engineer (RPE) (3) Note: The RPE’s written design criteria must be maintained locally and available for review Other Protection Systems(3) Acceptable Shoring: Timber Hydraulic Other From OH&S’s Charts Engineered Data Acceptable Shielding: Single trench box Stacked trench boxes (Note: Top edge of shield must extend 0.46 meters above grade) Is the soil contaminated: Yes No If yes, with what? PPM Excavating in or near roads(6): Yes No If yes, has the Road Dept been notified: Yes No List all traffic control devices: Will water removal be needed: Yes No How will water be removed? Atmospheric check if over 1.2 meters or 4’ deep – Name of Equip? O2 % LFL / LEL % Spoil Pile - minimum 1 meter or 3 feet back: Yes No Comments: Competent person signature: Notes: Initiate inspections and take appropriate actions regardless of depth when soils indicate signs of stress or cave-in. Every inspection requires at least 1 visual test and 1 manual test. Sloping or benching excavations greater than 6.10 meters or 20 feet deep or any trench 3.96 m deep in type 4 soils shall be designed & approved by a professional engineer registered within the same province as the excavation. Shoring & shield equipment used in excavations greater than 6.10 meters or 20 feet shall be designed & approved by a registered professional engineer. H denotes horizontal, V denotes vertical. All spoil piles, material or equipment must be a minimum of 1 meter or 3 feet from the edge of the excavation. A written Temporary Traffic Control Plan shall be developed and on site if any work is within 4.57 meters or 15 feet of a road. |

|  | EXCAVATION INSPECTION REPORT (Canada) |
| --- | --- |
| Attachment A The following is from the Saskatchewan Occupational Health and Safety Regulations and should be used in Canada. “Type 1 soil” means soil that most closely exhibits the following characteristics: is hard in consistency, very dense in compactive condition and, if a standard penetration test is performed, has a standard penetration resistance of greater than 50 blows per 30 cm (1 foot) can be penetrated only with difficulty by a small, sharp object has a dry appearance has no signs of water seepage can be excavated only by mechanical equipment does not include previously excavated soils “Type 2 soil” means soil that most closely exhibits the following characteristics: is very stiff in consistency, dense in compactive condition and, if a standard penetration test is performed, has a standard penetration resistance of 30 to 50 blows per 30 cm (1 foot) can be penetrated with moderate difficulty by a small, sharp object is difficult to excavate with hand tools has a low to medium natural moisture content and a damp appearance after it is excavated has no signs of water seepage does not include previously excavated soils “Type 3 soil” means soil that most closely exhibits the following characteristics: (A) is stiff in consistency, compact in compactive condition and, if a standard penetration test is performed, has a standard penetration resistance of 10 to 29 blows per 30 cm (1 foot) (B) can be penetrated with moderate ease by a small, sharp object (C) is moderately difficult to excavate with hand tools (D) exhibits signs of surface cracking (E) exhibits signs of localized water seepage; or is previously excavated soil that does not exhibit any of the characteristics of type 4 soil “Type 4 soil” means soil that exhibits any of the following characteristics: (A) is firm to very soft in consistency, loose to very loose in compactive condition and, if a standard penetration test is performed, has a standard penetration resistance of less than 10 blows per 30 cm (1 foot); (B) is easy to excavate with hand tools (C) is cohesive soil that is sensitive and, on disturbance, is slightly reduced in internal strength (D) is dry and runs easily into a well-defined conical pile (E) has a wet appearance and runs easily or flows (F) is granular soil below the water table, unless the soil has been dewatered (G) exerts substantial hydraulic pressure when a support system is used; or is previously excavated soil that exhibits any of the characteristics mentioned above Guidelines Depending on Soil Type In type 1 or type 2 soil, the walls are sloped to within 1.2 m (4 feet) of the bottom of the excavation or trench, with a slope at an angle not steeper than one horizontal to one vertical, or 45° measured from the horizontal. In type 3 soil, the walls are sloped from the bottom of the excavation or trench, with a slope at an angle not steeper than one horizontal to one vertical, or 45° measured from the horizontal. In type 4 soils, the walls are sloped from the bottom of the excavation or trench, with a slope at an angle not steeper than three horizontal to one vertical, or 19° measured from the horizontal. Note: Where an excavation or trench contains more than one type of soil, the soil must be classified as the soil type with the highest number. Note: An employer or contractor shall ensure that a temporary protective structure in a trench more than 20 feet (6 m) in Type 1, 2, or 3 soils or in a trench more than 13 feet (4 m) deep in type 4 soil is designed and certified as safe by a professional engineer. |